## Slide 1
Introduction
Course 2
2019
INFO 802
Master Advanced Mechatronics
Luc Marechal

## Slide 2: Create first node Hello World (C++)
with roscpp (C++ Client Library)
> cd ~/catkin_ws/src/beginner_tutorials/src
> sudo gedit hello_cpp.cpp
ROS main header file include
Create the node
Package.xml
src
beginner_tutorials
CMakeLists.txt
hello_cpp.cpp
#include <ros/ros.h>
int main(int argc, char** argv)
{
ros::init(argc, argv, "hello_world");
ros::NodeHandle nodeHandle;
ros::Rate loopRate(10);
unsigned int count =0;
while (ros::ok()) {
ROS_INFO_STREAM("Hello World " << count);
ros::spinOnce();
looprate.sleep();
count++;
}
return 0;
}

## Slide 3: Create first node Hello World
with roscpp (C++ Client Library)
#include <ros/ros.h>
int main(int argc, char** argv)
{
ros::init(argc, argv, "hello_world");
ros::NodeHandle nodeHandle;
ros::Rate loopRate(10);
unsigned int count =0;
while (ros::ok()) {
ROS_INFO_STREAM("Hello World " << count);
ros::spinOnce();
looprate.sleep();
count++;
}
return 0;
}

## Slide 5: Building first node Hello World (C++)
  cmake_minimum_required(VERSION 2.8.3)
  project(beginner_tutorials)
  ## Find catkin macros and libraries
  find_package(catkin REQUIRED COMPONENTS roscpp rospy std_msgs)
  ## Declare ROS messages and services
  # add_message_files(FILES Message1.msg Message2.msg)
  # add_service_files(FILES Service1.srv Service2.srv)
  ## Generate added messages and services
  # generate_messages(DEPENDENCIES std_msgs)
  ## Declare catkin package
  catkin_package()
  ## Specify additional locations of header files
  include_directories(${catkin_INCLUDE_DIRS})
  ## Declare a cpp executable
  add_executable(hello_cpp src/hello_cpp.cpp)
  ## Specify libraries to link a library or executable target against
  target_link_libraries(hello_cpp ${catkin_LIBRARIES})
Before building your node, you should modify the CMakeLists.txt in the package
Package.xml
src
beginner_tutorials
CMakeLists.txt
hello_cpp.cpp
Customizing CMakeLists.txt
specifies the executable to be created after the build
links libraries and executables

## Slide 6: Building first node Hello World (C++)
  <?xml version="1.0"?>
  <package format="2">
  <name>beginner_tutorials</name>
  <version>0.1.0</version>
  <description>The beginner_tutorials package</description>
  <maintainer email=“luc@univ-smb.fr">Luc Mare</maintainer>
  <license>BSD</license>
  <url type="website">http://wiki.ros.org/beginner_tutorials</url>
  <author email=“luc@univ-smb.fr">Luc Marechal</author>
  <buildtool_depend>catkin</buildtool_depend>
  <build_depend>roscpp</build_depend>
  <build_depend>rospy</build_depend>
  <build_depend>std_msgs</build_depend>
  <exec_depend>roscpp</exec_depend>
  <exec_depend>rospy</exec_depend>
  <exec_depend>std_msgs</exec_depend>
  </package>
Before building your node, you should modify the generated package.xml in the package
Package.xml
src
Beginner_tutorials
CMakeLists.txt
hello_cpp.cpp
Customizing package.xml

## Slide 7: Building first node Hello World (C++)
> cd ~/catkin_ws
> catkin_make beginner_tutorials
  > cd ~/catkin_ws
  > source ./devel/setup.bash
> rosrun beginner_tutorials hello_cpp
Build package
Run your node
Make sure you have sourced your workspace's setup.bash file

## Slide 8: Create first node Hello World (Python)
with rospy (Python Client Library)
#!/usr/bin/env python
# -*- coding utf-8 -*-
__author__ = "Luc Marechal"
__copyright__ = "The Hello World Project copyright"
__credits__ = “myself"
__license__ = "GPL"
__version__ = "0.0.1"
__maintainer__ = "Luc Marechal"
__email__ = "luc@univ-smb.fr"
__status__ = "Development"
import rospy
rospy.init_node(‘hello_python’)
rate = rospy.Rate(10)
while not rospy.is_shutdown():
print “Hello World”
rate.sleep()
> cd ~/catkin_ws/src/beginner_tutorials/scripts
> sudo gedit hello_python.py
This is the shebang. It lets the OS know that this is a Python file, and that it should be passed to the Python interpreter
Create the node
Package.xml
scripts
beginner_tutorials
CMakeLists.txt
hello_python.py

## Slide 9: Building first node Hello World (Python)
with rospy (Python Client Library)
Give execution permissions to the file
http://www2.ece.ohio-state.edu/~zhang/RoboticsClass/docs/ECE5463_ROSTutorialLecture1.pdf
Make the file executable
  > cd ~/catkin_ws
  > source ./devel/setup.bash
> rosrun beginner_tutorials hello_python.py
Make sure you have sourced your workspace's setup.bash file
Run your node
> chmod +x hello_python.py
Extension needed

## Slide 10: Create Nodes Summary
Create your .cpp file in /src folder
Customize CMakeLists.txt and package.xml files
Build the package which contains the node
Source your workspace
Run your node
Create your .py file in /scripts folder
Make the file executable
Source your workspace
Run your node with the .py extention
Package.xml
scripts
Package
CMakeLists.txt
Node.py
Package.xml
src
CMakeLists.txt
Node.cpp
Package

## Slide 11: Creating a Publisher and a Subscriber Node (C++)
Package.xml
src
beginner_tutorials
CMakeLists.txt
First_Publisher_Node.cpp
Writing the publisher Node
> cd ~/catkin_ws/beginner_tutorials/src
> gedit First_Publisher_Node.cpp
Edit a cpp file
This node will publish an integer value on a topic called numbers
  #include "ros/ros.h"
  #include "std_msgs/Int32.h"
  #include <iostream>
  int main(int argc, char **argv)
  {
  ros::init(argc, argv,"First_Publisher_Node");
  ros::NodeHandle node_obj;
  ros::Publisher number_publisher = node_obj.advertise<std_msgs::Int32>("numbers",10);
  ros::Rate loop_rate(10);
  int number_count = 0;
  while (ros::ok())
  {
  std_msgs::Int32 msg;
  msg.data = number_count;
  ROS_INFO("%d",msg.data);
  number_publisher.publish(msg);
  ros::spinOnce();
  loop_rate.sleep();
  ++number_count;
  }
  return 0;
  }

## Slide 12: Creating a Publisher and a Subscriber Node (C++)
Examining the publisher Node
Includes all the headers necessary to use the most comon public pieces of ROS system.
We will send an integer value, so we need to include this header. Standard message definition for integer datatype.
Initialize ROS. Has to be called before other ROS functions. Specifies the name of our node (must be unique in a running system).
The Nodehandle object is the access for communication with the ROS system.
Tell the master that we are going to be publishing a message of type Int32 on the topic my_numbers.
ros::Rate is a helper class to run loops a desired frequency (here 10 Hz).
  #include "ros/ros.h"
  #include "std_msgs/Int32.h"
  #include <iostream>
  int main(int argc, char **argv)
  {
  ros::init(argc, argv,"First_Publisher_Node");
  ros::NodeHandle node_obj;
  ros::Publisher number_publisher = node_obj.advertise<std_msgs::Int32>("numbers",10);
  ros::Rate loop_rate(10);
  int number_count = 0;
  while (ros::ok())
  {
  std_msgs::Int32 msg;
  msg.data = number_count;
  ROS_INFO("%d",msg.data);
  number_publisher.publish(msg);
  ros::spinOnce();
  loop_rate.sleep();
  ++number_count;
  }
  return 0;
  }

## Slide 13: Creating a Publisher and a Subscriber Node (C++)
  #include "ros/ros.h"
  #include "std_msgs/Int32.h"
  #include <iostream>
  int main(int argc, char **argv)
  {
  ros::init(argc, argv,"First_Publisher_Node");
  ros::NodeHandle node_obj;
  ros::Publisher number_publisher = node_obj.advertise<std_msgs::Int32>("numbers",10);
  ros::Rate loop_rate(10);
  int number_count = 0;
  while (ros::ok())
  {
  std_msgs::Int32 msg;
  msg.data = number_count;
  ROS_INFO("%d",msg.data);
  number_publisher.publish(msg);
  ros::spinOnce();
  loop_rate.sleep();
  ++number_count;
  }
  return 0;
  }
Examining the publisher Node
ros::ok() checks if a node should continue running
Returns false if SIGINT is received (Ctrl + C) or ros::shutdown() has been called
This is an infinite while loop, and it quits when we press Ctrl + C. The ros::ok() function returns zero when there is an interrupt; this can terminate this while loop
Creates an integer ROS message, and the second line assigns an integer value to the message. Here, data is the field name of the msg object:
This will print the message data. This line is used to log the ROS information.
Publish the message to the topics numbers. Broadcast the message to anyone who is connected
ROS::spinOnce() processes incoming messages via callbacks

## Slide 14: Creating a Publisher and a Subscriber Node (C++)
Package.xml
src
beginner_tutorials
CMakeLists.txt
First_Subscriber_Node.cpp
Writing the subscriber Node
> cd ~/catkin_ws/beginner_tutorials/src
> gedit First_Subscriber_Node.cpp
Edit a cpp file
This node will subscribe to an integer value on a topic called numbers
  #include "ros/ros.h"
  #include "std_msgs/Int32.h"
  #include <iostream>
  void number_callback(const std_msgs::Int32::ConstPtr& msg) {
  ROS_INFO("Received [%d]",msg->data);
  }
  int main(int argc, char **argv) {
  ros::init(argc, argv,"First_Subscriber_Node");
  ros::NodeHandle node_obj;
  ros::Subscriber number_subscriber =
  node_obj.subscribe("numbers",10,number_callback);
  ros::spin();
  return 0;
  }

## Slide 15: Creating a Publisher and a Subscriber Node (C++)
Examining the subscriber Node
This is a callback function that will execute whenever a data comes to the /numbers
topic. Whenever a data reaches this topic, the function will call and extract the value and print it on the console.
Subscribe to the numbers topic with the master. ROS will call the number_callback() function whenever a new message arrives. The 2nd argument is the queue size, in case we are not able to process messages fast enough. In this case, if the queue reaches 10 messages, we will start throwing away old messages as new ones arrive.
  #include "ros/ros.h"
  #include "std_msgs/Int32.h"
  #include <iostream>
  void number_callback(const std_msgs::Int32::ConstPtr& msg) {
  ROS_INFO("Received [%d]",msg->data);
  }
  int main(int argc, char **argv) {
  ros::init(argc, argv,"First_Subscriber_Node");
  ros::NodeHandle node_obj;
  ros::Subscriber number_subscriber =
  node_obj.subscribe("numbers",10,number_callback);
  ros::spin();
  return 0;
  }
ros::spin() is an infinite loop in which the node will wait in this step. The code will calling message callbacks as fast as possible. The node will quit only when we press the Ctrl+ C key.

## Slide 16: Creating a Publisher and a Subscriber Node (C++)
Building the nodes
> cd ~/catkin_ws/beginner_tutorials/src
> gedit First_Publisher_Node.cpp
Edit a cpp file
This node will publish an integer value on a topic called numbers

## Slide 17: Building Publisher and a Subscriber Node (C++)
  …
  ## Declare a cpp executable
  add_executable(First_Publisher_Node src/First_Publisher_Node.cpp)
  add_executable(First_Subscriber_Node src/First_Subscriber_Node.cpp)
  ## Dependencies
  add_dependencies(First_Publisher_Node beginner_tutorials_generate_messages_cpp)
  add_dependencies(First_Subscriber_Node beginner_tutorials_generate_messages_cpp)
  ## Specify libraries to link a library or executable target against
  target_link_libraries(First_Publisher_Node ${catkin_LIBRARIES})
  target_link_libraries(First_Subscriber_Node ${catkin_LIBRARIES})
  …
Before building your node, you should modify the CMakeLists.txt in the package
Package.xml
src
beginner_tutorials
CMakeLists.txt
First_Subscriber_Node.cpp
Building the nodes
> cd ~/catkin_ws
> catkin build
> source ./devel/setup.bash
Build all pakages
First_Publisher_Node.cpp

## Slide 18: Creating a Publisher and a Subscriber Node (Python)
The publisher node publishes a message of type Int32 on the topic named numbers
The subscriber node subscribes to the topic named numbers on which the message is of type Int32

## Slide 19: Creating a Publisher and a Subscriber Node (Python)
Writing the publisher Node
> cd ~/catkin_ws/beginner_tutorials/
> mkdir scripts
> cd scripts
> sudo gedit First_Publisher_Node.py
Edit a .py file in scripts folder
This node will publish an integer value on a topic called numbers
  #!/usr/bin/env python
  import rospy
  from std_msgs.msg import Int32
  def First_Publisher_Node():
  pub = rospy.Publisher('numbers', Int32, queue_size=10)
  rospy.init_node('First_Publisher_Node', anonymous=True)
  rate = rospy.Rate(10) # 10hz
  number_count=0
  while not rospy.is_shutdown():
  rospy.loginfo(number_count)
  pub.publish(number_count)
  rate.sleep()
  number_count += 1
  if __name__ == '__main__':
  try:
  First_Publisher_Node()
  except rospy.ROSInterruptException:
  pass
Package.xml
scripts
beginner_tutorials
CMakeLists.txt
First_Publisher_Node.py

## Slide 20: Creating a Publisher and a Subscriber Node (Python)
  #!/usr/bin/env python
  import rospy
  from std_msgs.msg import Int32
  def First_Publisher_Node():
  pub = rospy.Publisher(‘numbers', Int32, queue_size=10)
  rospy.init_node('First_Publisher_Node', anonymous=True)
  rate = rospy.Rate(10) # 10hz
  number_count=0
  while not rospy.is_shutdown():
  #rospy.loginfo(number_count)
  pub.publish(number_count)
  rate.sleep()
  number_count += 1
  if __name__ == '__main__':
  try:
  First_Publisher_Node()
  except rospy.ROSInterruptException:
  pass
Examining the publisher Node
Every Python ROS Node will have this declaration at the top.
You need to import rospy if you are writing a ROS Node.
std_msgs.msg import is so that we can reuse the std_msgs/Int32 message type
The node is publishing to the numbers topic using the message type Int32
The queue_size argument limits the amount of queued messages if any subscriber is not receiving them fast enough.
anonymous = True ensures that your node has a unique name by adding random numbers to the end of NAME.
Helper class to run loop at desired frequency (here 10 Hz)

## Slide 21: Creating a Publisher and a Subscriber Node (Python)
  rospy.Publisher(name of the topic, message type, queue size)
Examining the publisher Node
queue size: this is the size of the outgoing message queue used for asynchronous publishing
More info
http://wiki.ros.org/rospy/Overview/Publishers%20and%20Subscribers

## Slide 22: Creating a Publisher and a Subscriber Node (Python)
Writing the subscriber Node
> cd ~/catkin_ws/beginner_tutorials/scripts
> sudo gedit First_Subscriber_Node.py
Edit a .py file in scripts folder
This node will subscribe to an integer value on a topic called numbers
  #!/usr/bin/env python
  import rospy
  from std_msgs.msg import Int32
  def callback(data):
  rospy.loginfo(rospy.get_caller_id() + "I heard %s", data.data)
  def First_Subscriber_Node():
  # In ROS, nodes are uniquely named. If two nodes with the same name are launched, the
  # previous one is kicked off. The anonymous=True flag means that rospy will choose a
  # unique name for our 'listener‘ node so that multiple listeners can run simultaneously.
  rospy.init_node('First_Subscriber_Node', anonymous=True)
  rospy.Subscriber('numbers', Int32, callback)
  rospy.spin()
  if __name__ == '__main__':
  First_Subscriber_Node()
Package.xml
scripts
beginner_tutorials
CMakeLists.txt
First_Publisher_Node.py
First_Subscriber_Node.py

## Slide 23: Creating a Publisher and a Subscriber Node (Python)
  #!/usr/bin/env python
  import rospy
  from std_msgs.msg import Int32
  def callback(data):
  rospy.loginfo(rospy.get_caller_id() + "I heard %s“, data.data)
  def First_Subscriber_Node():
  # In ROS, nodes are uniquely named. If two nodes with the same name are launched, the
  # previous one is kicked off. The anonymous=True flag means that rospy will choose a
  # unique name for our 'listener‘ node so that multiple listeners can run simultaneously.
  rospy.init_node('First_Subscriber_Node', anonymous=True)
  rospy.Subscriber('numbers', Int32, callback)
  rospy.spin()
  if __name__ == '__main__':
  First_Subscriber_Node()
Examining the subscriber Node
*Callback : function that is passed as an argument to other function
When new messages are received, callback* is invoked with the message as the first argument.
rospy.spin(): simply keeps the node from exiting until the node has been shutdown
rospy.loginfo: logs messages to the filesystem
The anonymous=True flag tells rospy to generate a unique name for the node so that you can have multiple listener.py nodes run easily

## Slide 24: Creating a Publisher and a Subscriber Node (Python)
  rospy.Subscriber(name of the topic, message type, callback function)
Examining the subscriber Node

## Slide 25: Creating a Publisher and a Subscriber Node (Python)
Building the nodes
> cd ~/catkin_ws
> catkin_make beginner_tutorials
  > cd ~/catkin_ws
  > source ./devel/setup.bash
> rosrun beginner_tutorials First_Publisher_Node.py
> rosrun beginner_tutorials First_Subscriber_Node.py
Build package
(we use Cmake as the build system even for Python nodes)
Run your nodes
Make sure you have sourced your workspace's setup.bash file
> chmod +x First_Subscriber_Node.py
> chmod +x First_Publisher_Node.py
Make the node executable (for Python only)
Package.xml
scripts
beginner_tutorials
CMakeLists.txt
First_Publisher_Node.py
First_Subscriber_Node.py

## Slide 26: ROS Launch
Imagine a scenario in which we have to launch 10 or 20 nodes for a robot.
It will be difficult if we run each node in a terminal one by one !!!

## Slide 27: ROS Launch
launch is a tool for launching multiple nodes (as well as setting parameters)
written in XML but file suffix: *.launch
the launch file needs to be located a folder named “launch” inside de package folder
If not yet running, launch automatically starts a roscore
Example
More info
http://wiki.ros.org/roslaunch
Package.xml
scripts
beginner_tutorials
CMakeLists.txt
First_Publisher_Node.py
First_Subscriber_Node.py
src
chat.launch
launch
The file chat.launch is created in order to launch the node : First_Publisher_Node.py and First_Subscriber_Node.py

## Slide 28: ROS Launch
Start a launch file from a package with
Or browse to the folder and start a launch file with
More info
http://wiki.ros.org/roslaunch
Example console output for:
> roslaunch beginner_tutorials chat.launch
> roslaunch [package_name] [file_name.launch]
> roslaunch [file_name.launch]

## Slide 29: ROS Launch
File Structure
output=“screen” makes the ROS log messages appear on the launch terminal window
<launch>
<node name="First_Publisher_Node" pkg="beginner_tutorials" type="First_Publisher_Node.py"/>
<node name="First_Subscriber_Node" pkg="beginner_tutorials" type="First_Subscriber_Node.py" output="screen"/>
</launch>
launch: root element of the Launch files. This is an XML document, and every XML document has one
node: each <node> tag specifies a node to be launched
name: name of the node (free to choose)
pkg: package containing the node
type: the executable name
output: specifies where to output log messages (screen -> consol, log -> log file)
chat.launch

## Slide 30: ROS Launch
Arguments

## Slide 31: ROS Launch
Including Other Launch Files

## Slide 32: ROS Launch
Running 2 nodes from Terminal

## Slide 33: ROS Launch
Running 2 nodes with roslaunch

## Slide 34: IDE for ROS
There is no best IDEs, only the IDE that works best for you !
Eclipse, Net Beans, Qt Creator: popular on Ubuntu ( )
Anaconda: nice interface ( )
but the ROS environment has to be set up and can be tedious
ROS Development Studio: only online ( )
Clion: user friendly and easy to setup ( )
RoboWare Studio: IDE especially designed for working with ROS. The installation is quite easy, and automatically detects and loads an ROS environment without additional configurations. It has different out-of-the-box features ( )

## Slide 35: RoboWare Installation
> cd /path/to/deb/file
> sudo dpkg -i roboware-studio_<version>_<architecture>.deb
Go to http://www.roboware.me/ and download the latest version of the software.
More info
http://www.roboware.me
Launch RoboWare in a console
> roboware-studio
That’s it !
Install deb file

## Slide 36: RoboWare Installation

## Slide 37: Setup a project in Sublime3
> sudo add-apt-repository ppa:webupd8team/sublime- text-3
> sudo apt-get update
> sudo apt-get install sublime-text-installer
Sublime 3 installation
More info
http://schulz-m.github.io/2016/07/12/sublime-for-catkin/
package_control installation
In Sublime : View > Show Console menu. Once open, paste the Python code
import urllib.request,os,hashlib; h = '6f4c264a24d933ce70df5dedcf1dcaee' + 'ebe013ee18cced0ef93d5f746d80ef60'; pf = 'Package Control.sublime-package'; ipp = sublime.installed_packages_path(); urllib.request.install_opener( urllib.request.build_opener( urllib.request.ProxyHandler()) ); by = urllib.request.urlopen( 'http://packagecontrol.io/' + pf.replace(' ', '%20')).read(); dh = hashlib.sha256(by).hexdigest(); print('Error validating download (got %s instead of %s), please try manual install' % (dh, h)) if dh != h else open(os.path.join( ipp, pf), 'wb' ).write(by)

## Slide 38: Setup a project in Sublime3
Setup project
Open sublime and then simply add your catkin_ws/src folder by using
Project -> Add Folder to Project, then save it as a project file in a location of your choice by Project -> Save Project as....
Build Tag definition
In SublimeType Alt + Shift + P and type install. Type ctags and put enter.
More info
http://schulz-m.github.io/2016/07/12/sublime-for-catkin/
> sudo apt-get install exuberant-ctags

## Slide 39: Setup a project in Sublime3
Build catkin package from Sublime
It is very straightforward to build catkin packages using catkin tools within sublime.
Simply install the catkin builder using the package manager. You can then either run it with ctrl + shift + p and then Build with: Catkin or using Tools -> Build.
ROS Msg File Syntax
Download the syntax file from Github and copy the file into
~.config/sublime-text-3/Packages/User.
Now you can simply select ROS message definition with View -> Syntax -> Open all with current extension as....
More info
http://schulz-m.github.io/2016/07/12/sublime-for-catkin/

## Slide 40: Further References
ROS Cheat Sheet
    https://www.clearpathrobotics.com/ros-robot-operating-system-cheat-sheet/
    https://kapeli.com/cheat_sheets/ROS.docset/
ROS Best Practices
    https://github.com/leggedrobotics/ros_best_practices/wiki
ROS Package Template
    https://github.com/leggedrobotics/ros_best_practices/tree/master/ros_package_template
ROS Wiki
    http://wiki.ros.org/
Installation
    http://wiki.ros.org/ROS/Installation
Tutorials
    http://wiki.ros.org/ROS/Tutorials
Available packages
    http://www.ros.org/browse/

## Slide 41: Relevant books

## Slide 42
Contact Information
Université Savoie Mont Blanc
Polytech’ Annecy Chambery
Chemin de Bellevue
74940 Annecy
France
https://www.polytech.univ-savoie.fr
Lecturer
Luc Marechal (luc.marechal@univ-smb.fr)
SYMME Lab (Systems and Materials for Mechatronics)